This page was exported from New Lead2pass PDF And VCE Ensure IT Exam Pass 100% [    https://www.dumps4microsoft.com    ]

Export date: Thu Apr 18 18:45:13 2024 / +0000 GMT

## [May 2018] Ensure Pass 200-155 Exam With Lead2pass New 200-155 Brain Dumps 164q

Quickly Pass 200-155 Test With Lead2pass New 200-155 Brain Dumps:;

https://www.lead2pass.com/200-155.html

QUESTION 31

Drag and Drop Question

Drag the WAAS component feature on the left to the corresponding function on the right.

Answer:

QUESTION 32

Refer to the exhibit below:

The figure shows CLI interface for VSAN configuration of Cisco MDS 9000 switch.

Which command is required to enter the configuration prompt for VSAN as shown in figure?

A.    config t

B.    vsan name

C.    vsan

D.    vsan database

Answer: D

Explanation:

Configuration terminal is not sufficient to enter vsan db configuration prompt. The vsan name command and ID can be created on vsan-db prompt which requires a vsan database command.

The vsan database command is used with vsan-db prompt to create a Vsan name and ID.

QUESTION 33

Which layer serves as the boundary between L2 and L3 links in a datacenter infrastructure?

A.    Access Layer

B.    Core Layer

C.    Aggregation Layer

D.    None of above

Answer: C

Explanation:

Access layer is the lowest layer used for physical connectivity. Core layer connects core to aggregation layers using L3 links.

Aggregation layer serves as an L2 and L3 boundary as well as a connecting point for firewall, etc.

QUESTION 34

Which of the following SAN devices provides an IOA feature?

A.    Cisco MDS 9000 16-Port Storage Services Node

B.    Cisco MDS 9100 Series Multilayer Fabric Switches

C.    Cisco MDS 9200 Series Multiservice Switches

D.    Cisco MDS 9148 Multilayer Fabric Switch

Answer: A

Explanation:

Cisco MDS 9000 16-Port Storage Services Node provides network host services such as I/O acceleration (IOA) which accelerates traffic and reduces response time. The Cisco MDS 9148 Multilayer Fabric Switch provides SAN extension but does not support IOA. Cisco MDS 9100 Series Multilayer Fabric Switches provide SAN extension but do not support IOA.

Cisco MDS 9200 Series Multiservice Switches provide SAN extension but do not support IOA.

QUESTION 35

Which feature monitors state transitions of components and processes in Cisco Unified Computing System?

A.    logical state arbiter

B.    discovery

C.    finite state machine

D.    state monitor

Answer: C

QUESTION 36

A UCS administrator has been tasked with creating a new server profile Which two pools can be used to assign Layer 2 interface information? (Choose two)

A.    Server

B.    Mac Address

C.    IP address

D.    UUD

E.    WWN

Answer: BE

QUESTION 37

Which management platform reduces server provisioning tome by automatically performing an inventory and deep discovery when new devices are attached?

A.    UCS Manager

B.    UCS Server

C.    CDP Manager

D.    Enterprise Manager

Answer: A

QUESTION 38

Which two standards enable Ethernet to support FCoE? (Choose two.)

A.    Priority Flow Control

B.    Virtual1 Extensible LAN

C.    Enhanced Transmission Selection

D.    Address Resolution Protocol

E.    virtual port channel and virtual device context

Answer: AC

QUESTION 39

Refer to the exhibit. Which statement is correct regarding this vPC environment?

A.    The vPC peer keep alive uses a non-VRF path.

B.    The ip arp synchronize is automatically configured when a vPC domain is created.

C.    The rote priority uses its default value.

D.    The system priority has been configured to a lower number than its default value.

Answer: D

QUESTION 40

A network engineer is configuring a pair of 6248 Fabric Interconnects, each with dual 10G uplinks to a parent switch. One design retirement is to ensure a specific server is able to use 10G of throughput to the LAN without contention from other servers within the 5108 chassis. Which technology will accomplish this?

A.    Port-Channels

B.    Unified Ports

C.    LAN Pin Groups

D.    System QoS Policy

Answer: C

200-155 dumps full version (PDF&VCE): https://www.lead2pass.com/200-155.html

Large amount of free 200-155 exam questions on Google Drive: https://drive.google.com/open?id=0B3Syig5i8gpDVFhnSlh5MURJTjQ

You may also need:

200-150 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDbUFVZERzemRpeEU

Post date: 2018-05-14 07:25:31

Post date GMT: 2018-05-14 07:25:31

Post modified date: 2018-05-14 07:25:31

Post modified date GMT: 2018-05-14 07:25:31

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com