This page was exported from New Lead2pass PDF And VCE Ensure IT Exam Pass 100% [    https://www.dumps4microsoft.com    ]

Export date: Wed Apr 17 20:44:16 2024 / +0000 GMT

## [April 2018] Free Lead2pass Cisco 352-001 PDF Dumps With New Update Exam Questions 510q

100% Pass Lead2pass 352-001 New Questions Free Version:;

https://www.lead2pass.com/352-001.html

QUESTION 21

Refer to the exhibit. All routers in this network are configured to place all interfaces in OSPF area 5. R3 is the designated router on the 10.1.5.0/24 network. If you examine the OSPF database on R4, what would the network (type 2) LSA, generated by R3, contain?

A.    a connection to 10.1.5.0/24 and links to R3, R2, and R1

B.    a connection to 10.1.5.0/24 and links to R2 and R1

C.    connections to 10.1.5.0/24 and 10.1.1.0/31

D.    no connections, R3 does not generate a network (type 2) LSA in this network

Answer: A

QUESTION 22

Refer to the exhibit. Which routes in this network will be installed in the routing table at router E?

A.    the OSPF route

B.    the EIGRP route

C.    the OSPF and EIGRP routes

D.    neither the OSPF nor the EIGRP route

Answer: C

QUESTION 23

An enterprise network manager has decided to dual-home two service providers for Internet connectivity. In order to provide optimal outbound routing, the full Internet routing table will be accepted from each provider. The enterprise has obtained address space and an AS to use in connecting to the Internet.

What is the simplest mechanism the network manager can use to prevent it from becoming a transit between the two service providers?

A.    Build a route filter that only allows the specific networks the enterprise owns to be advertised to

each of the service providers.

B.    Build a traffic filter that only allows traffic originating from the specific networks the enterprise

owns to be forwarded towards the service providers.

C.    Build a route filter that only allows networks with an empty AS path to be advertised to each of

the service providers.

D.    Build a route filter that only allows networks which are tagged with the LOCAL community to be

advertised to each of the service providers.

Answer: C

QUESTION 24

Which statement correctly describes how MTU mismatches are addressed in the IS-IS neighbor-formation process?

A.    IS-IS checks the locally configured MTU against the MTU advertised in neighbor hello packets.

B.    IS-IS checks the locally configured MTU against the MTU advertised in neighbor LSPs.

C.    IS-IS does not check for MTU mismatches when forming a neighbor relationship.

D.    IS-IS pads hellos, so neighbor relationships will not be formed on links with mismatched MTUs.

Answer: D

QUESTION 25

Which statement is true about connecting an IP multicast domain that is operating in PIM dense mode to a PIM sparse mode domain?

A.    The interconnection must be made at the rendezvous point of the PIM sparse mode domain.

B.    The connection can be made at any location in the network, as PIM sparse mode will inter-operate

seamlessly with PIM dense mode.

C.    PIM dense mode and sparse mode domains are not inter-operable and cannot be connected.

D.    The connection can be made at any location in the network, but PIM sparse mode and PIM dense

mode cannot inter-operate; IGMP must be used to provide the interconnection.

Answer: A

QUESTION 26

Two MPLS service providers (SP1 and SP2) are offering inter-provider RFC 2547/4364-based IP-VPN service to an enterprise customer. IP traffic among some of the customer's sites has to traverse both of the service providers. The service providers and the enterprise do not know what the minimum MTU is along the end-to-end path.

What could be done to guarantee that large packets are not dropped for MTU-related reasons?

A.    enable Path MTU Discovery on all devices within SP1 and SP2

B.    enable Path MTU Discovery on all devices within the enterprise

C.    configure the IP sender or senders to set the DF flag in the IP header

D.    configure the IP sender or senders to clear the DF flag in the IP header

Answer: B

QUESTION 27

Refer to the exhibit. R2 and R3 are running EBGP and are learning Network A and Network B. R2 and R3 are also running IBGP to exchange Network A and Network B. OSPF is IGP. R2 and R3 are advertising default routes. R1 and R4 can send and receive traffic from Network A and Network B respectively. However, Network A cannot send traffic to Network B.

How can you solve this problem?

A.    create a tunnel between R2 and R3

B.    create a tunnel between R2 and R4

C.    create static default routes pointing from R1 and R4 to R2 and R3, respectively

D.    convert R3 and R2 to ABRs so that R1 and R4 can choose the closest ABR to exit the network

Answer: A

QUESTION 28

Which of these is a reason to carry routes that originate outside your network in an EGP, such as BGP, rather than in your IGP, such as OSPF, EIGRP, or IS-IS?

A.    to provide better control over the distribution of the default route inside your network

B.    to prevent failures outside your network from impacting your internal network operation

C.    to provide faster convergence to destinations outside your network

D.    to provide a growth path for the core of your network

Answer: B

352-001 dumps full version (PDF&VCE): https://www.lead2pass.com/352-001.html

Large amount of free 352-001 exam questions on Google Drive: https://drive.google.com/open?id=0B3Syig5i8gpDaUphM0lMOWRjUU0

You may also need:

200-310 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDUE9zeHd2YUFFNUE

300-101 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDbHBiVVk1ZVhpOGc

300-115 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDM0pqaFJWUXVuM2M

300-320 exam dumps: https://drive.google.com/open?id=0B3Syig5i8gpDUGlzdWdZNHUwZ28

Post date: 2018-04-11 05:47:00

Post date GMT: 2018-04-11 05:47:00

Post modified date: 2018-04-11 05:53:23

Post modified date GMT: 2018-04-11 05:53:23

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com